## Slide 1: Save time and space in body motor design
Madison Eaker - body electronics and lighting systems
Featuring door, roof, trunk and seat applications
Notes: I’m Madison Eaker, and I cover body electronics and lighting systems at Texas Instruments. In this presentation, I’m going to talk about how you can achieve smoother, more precise motion in your body motor design by replacing relays with MOSFETS in your H-bridge circuit and use integrated circuits motor drivers to reduce design time and complexity. Let’s get started.

## Slide 2: Automotive body motors at a glance
2
Notes: Body motors are located throughout a vehicle and offer passengers a range of features that improve their physical comfort as well as convenience. In most vehicles there are more than 20 body motors.
For today’s presentation, let’s take a look at four important body motors: the door, seats, sunroof and the trunk (or boot, depending on where you’re from). I’ll discuss some of the beneficial analog functions which can be integrated to simplify your body motor design.

## Slide 3: Crossing the H-bridge
Relays operate switches in an H-bridge
Make a “clicking” sound
Lack precise motor position and control
MOSFET switching is faster than relays
Allow PWM for speed control
Higher reliability
Notes: On the surface, the door, seats, sunroof and trunk are quite different, but movement is the commonality. And if you’re watching this, you know that the motion must be smooth, precise and easy for drivers and passengers to engage.
Traditionally, the electric motors for these applications are controlled using switches arranged in the shape of the letter “H,” and looks like this. It’s easy to remember that this is called an H-bridge.
In older designs, relays were used as the switches, but most new designs now use MOSFETs, due to their advantages in reliability, switching speed, and controllability.

## Slide 4: The switch to MOSFETs
One big advantage: Enhanced motor control and performance
Suppress electromagnetic interference (EMI) from pulse-width-modulated (PWM) signals.
Current sensing to detect malfunctions and determine position and commutation.
Power-off braking to prevent damage to electronic components.
Diagnostics and protection to detect circuit continuity faults such as open and short circuits.
Thermal management to address heat generated from the current.
Notes: Using MOSFETs as switches presents new technical challenges in electronic control module designs, including electromagnetic interference (EMI) and thermal management, current sensing, power-off braking, and diagnostics and protection. The broad portfolio of integrated circuit (IC) motor driver products developed by Texas Instruments integrate analog features that help electronic control module designers overcome these challenges while reducing solution size and shortening development times. Moreover, the products range from single half bridge products to multiple H-bridge gate driver products that all you to easily scale your designs based on specific design implementation. In this presentation, we will discuss specific analog features integrated in motor drivers ICs that help address these design challenges.

## Slide 5: Mitigating EMI with an H-bridge
DRV8706-Q1
DRV8706-Q1 EVM
Control speed with pulse width modulation
Low electromagnetic emissions
Pass CISPR tests
Design challenges
On-line technical information at training.ti.com
Videos and Demos
NEW
N
Other IC options: DRV8106-Q1, DRV8714-Q1, DRV8718-Q1
DRV8706-Q1
NEW
Simplify EMI optimizations using Texas Instruments’ Smart Gate Drive and Spread Spectrum Clocking feature!
NEW
Notes: The MOSFETs in the H-Bridge may be driven using PWM signals which can result in electromagnetic interference or EMI. This is especially true for relatively high-current applications such as window lift motors. Control module designers use filters, optimal layout and PWM edge shaping to mitigate EMI.
Gate driver products such as the DRV8106-Q1 single half H-Bridge driver, DRV8705-Q1 dual half H-Bridge driver, and DRV8719-Q1 multi-half H-Bridge gate drivers for brushed DC motors, and the DRV8343-Q1 3-phase gate driver for brushless DC motors all integrate smart gate drive technology. This technology is specifically used to control the shape of the PWM rising and falling edges and offers designers the flexibility to choose the shape that achieves EMI performance while not degrading thermal performance of the MOSFETs.
The dual half H-bridge BDC motor gate driver products are used to control loads such as window motor and roof motor, the multi half H-Bridge is ideally suited for seat applications which has typically many motors.

## Slide 6: Thermal design with motor drivers
DRV8705-Q1
DRV8705-Q1 EVM
Drive high power motors efficiently
Operate at high temperatures
Low power losses
Design challenges
On-line technical information at training.ti.com
Application notes
N
DRV8705-Q1
NEW
From Integrated FET Motor Drives to multichannel gate drivers TI has the right device for your design
NEW
Notes: Thermal design is important due to the heat generated as an electric motor’s current flows through the MOSFETs in an H-bridge. Motors which adjust the position of seats typically have heavy loads to move, causing high currents and potential thermal issues.
With motor-driver products you can choose to implement with MOSFET gate drivers plus discrete MOSFETs for high-current electric motors (such as power windows). The DRV8706-Q1 for single motors or DRV8718-Q1 for multiple motors enable electronic control module designers to achieve optimal thermal management.
Devices with integrated H-bridge MOSFETs, such as the DRV8873-Q1, DRV8874-Q1 and DRV8876-Q1, have different maximum current ratings and can drive low-current loads such mirror X/Y motors.
A three-phase BLDC motor driver such as the DRV10983-Q1 not only integrates the MOSFETs but also integrates the commutation algorithm. These integrated BLDC drivers are popular to drive ventilation fans in seats.

## Slide 7: Current sensing
DRV8873-Q1
DRV8873-Q1 EVM
Monitor motor current to detect faults
Motion feedback with ripple counting
In-line or low-side sensing
Design challenges
On-line technical information at training.ti.com
Application notes
N
Other IC options: DRV8871-Q1, DRV8874-Q1 DRV8876-Q1
TI motor drives eliminate the need for external current sense amplifier and more to reduce your BOM and cost!
Notes: Measuring the current flowing in electric motors can help detect motor malfunctions, determine motor position and for motor commutation. For example, current measurement is important in sunroof modules to detect motion and to identify motor stall faults due to obstacles. One common method to measure current in an electric motor is to use a resistor in the path of the current flow, and then amplify the voltage across the resistor using an amplifier.
BDC and BLDC motor gate-driver products should integrate a current-sense amplifier to amplify the voltage across the resistor. Some devices such as the DRV8706-Q1 even offer an in-line current-sense amplifier; that is, a single current-sense resistor can measure current flowing in the motor regardless of the direction of motor rotation. This is in contrast to a typical current-sense amplifier, which is used to measure the low side of an H-bridge and cannot infer the direction of motor rotation.
One common use of in-line current sensing is to measure BDC motor ripple. The measured in-line current is post-processed using either an analog circuit or software to infer the motor position, which is in turn used to control and regulate window, roof, trunk or seat positions.
One motor driver that is gaining interest for BLDC motor-driven windows and seat-base rotation control also integrates current-sense amplifiers.

## Slide 8: Power off braking
DRV8714-Q1
DRV8714-Q1 EVM
Movement of mechanical parts
Unpowered motors generate voltage
Protect drive circuits from dangerous levels
Design challenges
On-line technical information at training.ti.com
Application note
N
Other IC options: DRV8718-Q1
DRV8714-Q1
Integrated protection against back EMF when your system is On or OFF
Notes: In some systems, such as power lift gate, it is possible for the motor to be external driven in event that the user is manually moving the closure and the motor has not been clutched out of the mechanical system. This can generate a significant back-emf energy in the motor that can charge the dc link supply, raising the voltage, and sending current back to the battery.
A possible resolution is to actively brake the DC motor through the drive stage electronics, but there may be conditions where the drive stage electronics are not active such as in deep sleep.
In deep sleep, to reduce standby current, bridge FET drivers are disabled and H-bridges are high impedance. This allows energy to flow back into the supply through the bridge body diodes.
The DRV8714-Q1 and DRV8718-Q1 include a power-off braking feature that protects the drive circuit from high generated voltages and brakes the motion.

## Slide 9: Advanced diagnostics
Detect short-circuit faults to battery
Detect faults in drive circuit
Notify MCU for corrective action or safe mode
Design challenges
Detects load getting disconnected at power-up or while in motion.
Open Load Fault
Detects motor winding short-to-battery while the motor is not in motion and alerts the MCU promptly for corrective action.
Short to supply
Detects motor winding short-to-ground while the motor is not in motion and alerts the MCU promptly for corrective action.
Short to ground
DRV
MCU
!
Notes: BDC and BLDC gate drivers should integrate diagnostic circuits to detect circuit continuity faults such as open and short circuits. These circuits will prevent the MOSFETs from turning on in the presence of faults, thus protecting the control module from damage.
In addition to integration, products that offer failure-mode distribution and pin failure-mode analysis information can help you design a control module in compliance with the International Organization for Standardization 26262 automotive functional safety standard.

## Slide 10: Explore products
Control module | Load | Products
Door | Single window with BDC motor | DRV8705-Q1, DRV8706-Q1
 | Door lock motor Dual window with BDC motor | DRV8714-Q1, DRV8718-Q1, DRV8873-Q1
 | Single window with BLDC motor | DRV8343-Q1
 | Mirror X/Y motor Mirror fold motor | DRV8908-Q1, DRV8873-Q1
Roof | Roof motor | DRV8705-Q1, DRV8706-Q1
 | Multiple roof motor | DRV8714-Q1, DRV8718-Q1
Trunk | Single trunk lift BDC motor | DRV8705-Q1, DRV8706-Q1
 | Multiple trunk lift BDC motors | DRV8714-Q1, DRV8718-Q1
 | Single trunk lift BLDC motor | DRV8343-Q1
 | Trunk cinch motor | DRV8873-Q1
Seat | Seat position adjust motor | DRV8714-Q1, DRV8718-Q1
 | Lumbar support bladder pump motor | DRV8873-Q1, DRV8874-Q1
 | Seat ventilation motor | DRV10983-Q1
 | Seat base rotation motor | DRV8343-Q1
Notes: Texas Instruments automotive brushed DC and brushless DC motor products integrate analog features that simplify the design of control modules, reduce solution size and shorten development cycles. Further, the products are targeted for door, mirror, roof, trunk and seat applications. TI has a broad and scalable portfolio which is adaptable to the various car trim levels.
This table maps the products to the motors used in these applications.

## Slide 11: Thank you!